Neso Academy:
c is procedural language.
Middle level language
- direct access to memory though pointers.
- bit manipulation using bitwise operators.
- writing assembly code within c code.
wide variety of built-in functions, standard libraries and header files.

Variables:
declaration: announcing the properties of the variable to the compiler.
Properties:
1. size of the variable.
2. name of the variable.
int var;
datatype: how much space a variable is going to occupy In memory.
Var: name of the variable.

Size of integer:
depends on machine:
2 bytes: 16 bits.
4 bytes: 32 bits.
To know the size programatically:
use sizeof operator:
sizeof is a unary operator and not a function.
#include <stdio.h>

int main()
{
printf(“%d”, sizeof(int));
return 0;
}

range of integer:
at 2 bytes (16 bits machine)
unsigned range: 0 to 65535 (2^n -1)
signed range: -32768 to +32767
2’s complement range -(2^(n-1)) to +(2^(n-1) -1)

at 4 bytes (32 bits machine)
unsigned range: 0 to 4294967295
signed range: -2147483648 to +21147483647

int modifiers:
long and short:
if integer is 4 bytes, short int may be 2 bytes.
#include <stdio.h>

int main()
{
printf(“%d”, sizeof(short int));
return 0;
}
if integer is 4 bytes, long int may be 8 bytes.
#include <stdio.h>

int main()
{
printf(“%d”, sizeof(long int));
return 0;
}

Note: by default int some_variable_name; is signed integer variable.
unsigned int some_variable_name; allows only positive values.
1. sizeof(short) <= sizeof(int) <= sizeof(long).
2. writing signed int some_variable_name; is equivalent to int some_variable_name;
3. %d is used to print "signed integer".
4. %u is used to print "unsigned integer".
5. %ld is used to print "long integer" equivalent to "signed long integer".
6. %lu is used to print "unsigned long integer".
7. %lld is used to print "long long integer".
8. %llu is used to print "unsigned long long integer".

Exceeding the valid range of datatypes returns wrong values.

Character data type:
char some_variable_name = “N”;

#include <stdio.h>
int main()
{
char var = 65; // assigns character based on ASCII code.
printf(“%c\n”, var);
return 0;
}

size and range of character:
size: 1 byte = 8 bits.
Range: unsigned 0:255
signed: -128:+127
in traditional ASCII table, each character requires 7 bits.
In extended ASCII table, each character requires 8 bits.

Float → 4 bytes = 32 bits.	4 bytes (ubuntu 22.04 x64)
Double → 8 bytes = 64 bits.	8 bytes (ubuntu 22.04 x64)
Long Double → 12 bytes = 96 bits.	16 bytes (ubuntu 22.04 x64)
Size of these data types totally depends from system to system.

Float → IEEE 754 Single precision floating point.
Double → IEEE 754 Double Precision floating point.
Long Double → Extended Precision Floating point.

#include <stdio.h>
int main()
{
float var1 = 3.1415926535897932;
double var2 = 3.1415926535897932;
long double var3 = 3.1415926535897932;

printf("%ld\n", sizeof(float));
printf("%ld\n", sizeof(double));
printf("%ld\n", sizeof(long double));
printf("%.16f\n", var1);
printf("%.16f\n", var2);
printf("%.21Lf\n", var3);
}

#include <stdio.h>
int main()
{
int var = 4/9;
printf("%d\n", var);	// 0
float var1 = 4/9;
printf("%.2f\n", var1);	//0.00
float var2 = 4.0/9.0;
printf("%.2f\n", var2);	//0.44
}

Question 001:
#include <stdio.h>

int main(){
printf("%d", printf("%s", "Hello World!\n"));	//prints Hello World and Count.
return 0;
}

%s is used to print “String of Characters”.
Printf not only prints the content on the screen. It also returns the number of characters that it successfully prints on the screen.

#include <stdio.h>

int main(){
printf("%10s", "Hello"); //prints hello preceeded by 5 spaces.
return 0;
}

#include <stdio.h>

int main(){
char c = 255;
c = c +10;
printf("%d", c);	//prints 9
return 0;
}

correct definitions of integer:
I. signed int n;
II. signed n;
III. Unsigned n;
IV. long n;
V. long int n;
VI. long long n;

#include <stdio.h>

int main(){
unsigned i = 1;
int j = -4;
printf("%u", i+j); //prints integer value depends from machine to machine.
return 0;
}

-3 in 2s complement representation:
step 1: take 1s complement of 3
3 = 00000000 00000000 00000000 00000011
1s complement of 3 = 11111111 11111111 11111111 11111100
step 2: add 1 to the result. It will give:
11111111 11111111 11111111 11111101 = 4294967293

Scope:
scope = lifetime.
The area under which a variable is applicable or alive.
Strict Defintion:
a block or a region where a variable is declared, defined and used and when a block or a region ends, variable is automatically destroyed.

#include <stdio.h>
int main()
{
int var = 34;
printf("%d", var);	// scope of this variable is within main() function only. Therefore called Local to main() function.
return 0;
}
int fun()
{
printf("%d", var);	// trying to access variable “var” outside main() function.
}
#include <stdio.h>

int main()
{
int var = 3;
int var = 4;	// raises an error because var is already defined in same scope.
printf("%d\n", var);
printf("%d", var);
return 0;
}

another program:
#include <stdio.h>

int main()
{
int var = 3;
{
int var = 4;
printf("%d\n", var);
}
printf("%d", var);
return 0;
}
the above program prints 4 then 3

#include <stdio.h>
int fun();

int var = 10;	// global variable.

int main()
{
int var = 3;	// local variable.
printf("%d\n", var);
fun();
return 0;
}
int fun()
{
printf("%d", var);
}	// prints 3 then 10

Auto Modifier:
Auto means automatic:
Variables declared inside a scope by default are automatic variables.
Syntax: auto int some_var_name;
#include <stdio.h>	#include <stdio.h>
int main(){	int main(){
int var;	auto int var;
return 0;	return 0;
}	}
1. if you won’t initialize auto variable, by default it will be initialized with some garbage (random) value.

#include <stdio.h>

int main(){
auto int var;
printf("%d\n", var);	// prints random number.
return 0;
}

2. on the other hand, global variables by default initialized to 0.
#include <stdio.h>

int var;	// always initialized to 0;
int main(){
printf(“%d”, var);
return 0;
}

Extern Modifier:

int var;	extern int var;
declaration and definition	declaration

- extern is short name for external.
- used when a particular file needs to access a variable from another file.

- when we write extern some_data_type some_variable_name; no memory is allocated. Only property of variable is announced.
- multiple declarations of extern variable is allowed within the file. This is not the case with automatic variables.
- extern variables says to compiler “go outside from my scope and you will find the definition of the variable that I declared”.
- compiler believes that whatever the extern variable said is true and produce no error. Linker throws an error when it finds no such variable exist.
- when an external variable is initialized, then memory for this variable is allocated and it will be considered defined.

013. Variable Modifiers:
Memory:
Register memory	very small memory but fastest.
cache memory
main memory → primary memory.
Magnetic disks → auxillary memory
magnetic tapes → auxillary memory.	Slowest memory.

Register modifier:
syntax: register some_data_type some_variable_name

#include <stdio.h>
int main(){
register int var;
return 0;
}

What’s register modifier?
- register keyword hints the compiler to store a variable in register memory.
- this is done because access time reduces greatly for most frequently referred variables.
- this is the choice of compiler whether it puts the given variable in register or not.
- usually compiler themselves do the necessary optimizations.

- The static variable remains in memory even it’s declared within a block, on the other hand automatic variable is destroyed after the completion of function in which it was declared.
- static variable if declared outside the scope of any function will act like global variable but only within the file in which it was declared.
- you can only assign a constant literal or value to a static variable.

Constants in C:
Constant once defined can’t be modified later in the code.
-- Defining Constants:
→ using #define	syntax: #define NAME value
NAME → also called Macro, job of preprocessor to replace NAME with value.
→ using const

example:
#include <stdio.h>
#define PI 3.14159	// do not add semicolon at the end.

int main(){
printf(“%.5f”, PI);
return 0;
}

takeways of constants:
1. do not add semicolon at the end of constant.
2. choosing capital letters for NAME is good practice.
3. Whatever inside double quotes “” won’t get replaced.
4. we can use macros like function.

Example:
#include <stdio.h>
#define add(x, y) x+y

int main() {
printf(“addition of two numbers: %d”, add (4,3));
return 0;
}

5. we can write multiple lines using \

#include <stdio.h>
#define greater(x, y) if(x > y)\
printf(“%d is greater than %d”, x, y);\
else\
printf(“%d is lesser than %d”, x, y);
int main(){
greater (5 ,6);
return 0;
}

6. First expansion then evaluation:
#include <stdio.h>
#define add(x, y) x+y

int main(){
printf(“result of expression a * b + c is: %d”, 5 * add(4, 3)); // answer is 23.
}

7. some predefined macros like __DATE__, __TIME__ can print current date and time.
#include <stdio.h>

int main(){
printf(“Date: %s\n”, __DATE__); // date of compilation.
printf(“Time: %s\n”, __TIME__); // time of compilation.
return 0;
}

Constants part 2:
Define Constants using const.
Syntax:
const some_data_type some_variable_name

#include <stdio.h>

int main()
{
int var = 67;
var = 57;	// var will change to 57.
printf(“%d”, var);
}

------------------------------------------------------------
#include <stdio.h>

int main()
{
const int var = 67;
var = 60;	// will raise an error: assignment of read-only variable.
printf(“%d”, var);
}

#include <stdio.h>

int main(){
int var = 052; // preceeding 0 converts the number to octal.
printf(“%d”, var); // will print to 42 in decimal.
return 0;
}
=================================================

#include <stdio.h>

int main(){
int var = 052;
printf(“%o”, var); // will print 52 in octal.
return 0;
}
======================================

#include <stdio.h>

#define STRING "%s\n"
#define NESO "Welcome to neso academy!"

int main(){
printf(STRING, NESO); //prints: Welcome to neso academy!
return 0;
}

======================================

scanf:
stands for scan formatted string
accept character, string and numeric data from the user using standard input – keyboard.
scanf also use format specifiers like printf
for example:
%d to accept input of integer type.
%c to accept input of character type.
%s to accept a string.

Example:
int var;
scanf(“%d”, &var); // do not forget the ampersand symbol.

Why &?
while scanning the input, scanf needs to store that input data somewhere.
To store this input data, scanf needs to know the memory location of a variable.
& is also called as address-of operator.
&var	== address-of var

#include <stdio.h>

int main()
{
int a, b;
printf("Enter first number\n");
scanf("%d", &a);
printf("Enter second number\n");
scanf("%d", &b);
printf("%d + %d = %d\n", a, b, a+b);
return 0;
}

===================================
#include <stdio.h>

int main(){
int var = 0x43FF; //0x is a prefix for hexadecimal.
printf("%x", var); //will print 43FF.
return 0;
}
======================================
#include <stdio.h>

int main()
{
int var = 0X43FF; //0X --> prefix for hexadecimal.
printf("%d", var); //will print decimal.
return 0;
}
===========================================
#include <stdio.h>

static int i;
static int i = 27;
static int i;
int main(){
static int i;
printf("%d", i);	// will print 0
return 0;
}
==========================================

Memory layout of C program:
Two memory segments:
1. text/code segment: Contains machine code of the compiled program.
2. Data segment:
a. initialized: Global, extern, static (both local and global) const global variables.
I. Read only.
II. Read Write.
b. Uninitialized: uninitialized global, static (both local and global) constant global variables.
: uninitialized data segment also have read-only and read write sections.
(bss – Block started by symbol).
c. stack
d. heap.

020. Introduction to operators in c:
arithmetic operators → +,-,*,/,%
Increment / decrement operators → ++, --
Relational operators → ==, !=, <=, >=, < , >
Logical operators → &&, ||, !
Bitwise operators → &, ^, |, ~, >>, <<
Assignment operators → = , +=, -=, *=, /=, %=, <<=, >>=, &=, ^=, |=
other operators → ?=	&	*	sizeof()	,

021. Arithmetic operators:
arithmetic operators → +,-,*,/,%
all are binary operators → means two operands are required to perform operation.

#include <stdio.h>

int main(){
int a , b;
printf(“enter the first number\n”);
scanf(“%d”, &a);
printf(“Enter the second number\n”);
scanf(“%d”, &b);

printf(“a / b = %d\n”, a/b);
printf(“a / b = %d\n”, a%b);
return 0;
}

operator precedence and associativity:
Precedence	Operators	Associativity
Highest	*, /, %	Left to right
Lowest	+, -	Left to right

Note: Associativity is used only when two or more operators are of same precedence.
For example: +, -
Same precedence therefore, we use associativity.

#include <stdio.h>

int main(){
int a = 2, b = 3, c = 4, d = 5;
printf("a * b / c = %d\n", a*b/c);
printf("a + b - c = %d\n", a+b-c);
printf("a + b * d - c %% a = %d\n", a+b*d-c%a);
return 0;
}

022. Increment and decrement in C:
# Increment operator is used to increment the value of a variable by one.
Similarly, decrement operator is used to decrement the value of a variable by one.

Increment:	Decrement:
int a = 5;	int a = 5;
a++;	a--;

a = 6	a = 4

# increment and decrement operators:
* Both are unary operators:
- because they are applied on single operand.	a++; not a++a;
* pre and post:
- pre-increment operator:	++a;
- post-increment operator:	a++;
- pre-decrement operator:	--a;
- post-decrement operator:	a--;
* you cannot use rvalue before or after increment / decrement operator.
Example:
(a+b)++;	→ error!	++(a+b);	→ error!

Lvalue (left value): simply means an object that has an identifiable location in memory (i.e. having an address).
- in any assignment statement “lvalue” must have the capability to hold the data.
- lvalue must be a variable because they have the capability to store the data.
- lvalue cannot be a function, expression (like a+b) or a constant (like 3,4 etc).

Rvalue (right value): simply means an object that has no identifiable location in memory.

- Anything which is capable of returning a constant expression or value.
- Expressions like a +b will return some constant value.

Difference between pre & post increment and decrement:
pre- means first increment / decrement then assign it to another variable.
Post- means first assign it to another variable then increment/decrement.